## Slide 1: Chemical Mass Balance Software: EPA-CMB8.2
C. Thomas Coulter
Air Quality Modeling Group
Office of Air Quality Planning & Standards
U.S. Environmental Protection Agency
Research Triangle Park, NC 27711
John V. Scalco
Ideal Software, Inc.
P.O. Box 298
Apex, NC 27502

## Slide 2: Governing Equation
Ci is the ambient concentration of specie i;
aij is the fractional concentration of specie i in the emissions from source j;
Sj is the total mass concentration contributed by source j; and
p is the number of sources, and n is the number of species, with n ≥ p.
The Ci and aij are known and the Sj are found by a least squares solution of the overdetermined system of equations.

## Slide 3: FEATURES
Windows®-based, event-driven operations
Multiple arrays for fitting species and fitting sources
Britt-Luecke algorithm
Improved collinearity diagnostics
Better handling of VOC applications
Search for best fit
User-selected preferences
Notes: Windows®-based, event-driven operations: EPA-CMB8.2 makes full use of Windows® (32-bit) features, including a tabbed interface that facilitates the necessary progression for doing a CMB calculation. Commands may be executed with hot-keys or toolbar buttons, and features are described via mouse-overs and context sensitive on-line help screens. EPA-CMB8.2 also offers flexible options for input/output data formats. Input formats are compatible with output files from EPA’s source profile library SPECIATE (www.epa.gov/ttn/chief/).
Multiple arrays for fitting species and fitting sources: Up to ten indexed arrays of fitting source profiles and fitting species may be specified in input data selection files. Different arrays can be selected during EPA-CMB8.2 operation. Upon session exit, an option is provided to conveniently save (update) or rename selection files to reflect arrays that are added, modified or deleted during the session.
Britt-Luecke algorithm: A general solution to the least squares estimation problem that includes uncertainty in all the variables (i.e., the source compositions as well as the ambient concentrations) is available. While an approximation to the Britt-Luecke iteration scheme (Britt and Luecke, 1973) was used in CMB7, exercise of Britt-Luecke algorithm option in EPA-CMB8.2 allows solution without approximation.
Improved collinearity diagnostics: The uncertainty/similarity clusters have been replaced with a singular value decomposition eligible space treatment that allows the user to define an acceptable error and an acceptable collinearity among weighted source profiles.
Better handling of VOC applications: EPA-CMB8.2 gives the user control in adjusting collinearity parameters which in CMB7 are "hard-wired" and not necessarily optimum for every application. Values for these parameters were chosen in CMB7 to be compatible with characteristics of particulate mass measurements, but they may not be as well suited to CMB solutions involving VOC.
Search for best fit: Using a user-selected weighted optimization of performance measures, EPA-CMB8.2 can systematically check up to 10 possible paired combinations of fitting species and sources arrays as it searches for a maximum of an empirical composite measure. The best fit arrays are then indicated in their respective windows.
User-selected preferences: In EPA-CMB8.2, the user may set options for maximum iterations for convergence, eligible space tolerances, positions of decimal points in output, receptor concentration units, special calculation alternatives, and performance measure weights for use in Best Fit mode. The user may now easily retain or clear tagged samples following a multiple-sample (batch) run.

## Slide 4: FEATURES (cont’d)
Negative source contributions
Improved memory management
Upgraded linear algebra library
Versatile graphic display capability
Context-sensitive on-line help
Flexible input and output formats
File handling
Previously EPA-CMB8.2
Source PRofile selection file: SO*.sel PR*.sel
SPecies selection file: PO*.sel SP*.sel
Ambient Data (sample) selection file: DS*.sel AD*.sel
Notes: Negative source contributions: EPA-CMB8.2 calculations can be set to eliminate negative contributions.
Improved memory management: EPA-CMB8.2 memory is limited only by the available RAM on the host computer, not by pre-set memory limitations.
Upgraded linear algebra library: The linear algebra library that EPA-CMB8.2 uses to perform its effective variance, least-squares regressions has been updated with LAPACK v3.0.
Versatile graphic display capability: For ambient samples and source profiles, bar charts for species concentrations can be displayed within EPA-CMB8.2: very useful for inspection. These can be cut from their windows and pasted into other Windows documents.
Context-sensitive on-line help: Context-sensitive on-line help is accessible directly from the User Interface.
Flexible input and output formats: comma-separated value (CSV), xBASE (DBF), and worksheet (WKS) formats are supported as input files, in addition to the formatted, blank-delimited ASCII text files (TXT) supported by CMB7. Output files formats are ASCII and CSV (nicely portable to EXCEL).
File handling: EPA-CMB8.2 differs from CMB7 in several ways with regard to the files used by each. EPA-CMB8.2 does not support CMB6 style ambient data and source profile data files. Control File (formerly filenames file), source profile, ambient data, and sample selection file formats differ slightly from CMB7. CMB7 source profile and ambient concentration data files can be read directly by EPA-CMB8.2, however, so backward compatibility is assured. Different Control Files can be loaded during the same session, obviating the need to terminate the application. In EPA-CMB8.2 graphical output is not provided as HPGL text files.

## Slide 5: Launching the EPA-CMB-8.2 Software
Click

## Slide 6: Browse Dialog for Selecting a Control File
Click
We load the San Joaquin Valley Fine data set (Chow et al., 1992).

## Slide 7
Click

## Slide 8
Banner Page
via
Help | About
Click

## Slide 9
Control File name is echoed, as are any input files it directs to load.
Use browse boxes to add / change input files during a session.
Click
Click

## Slide 10
This parameter sets the maximum number of iterations EPA-CMB8.2 will attempt to arrive at a solution. If no convergence can be achieved, there is probably excessive collinearity for this sample and combination of fitting sources. Its value is adjusted via the spinners. (Must be >0; no theoretical upper limit; default = 20)

## Slide 11
Allows the eligible space collinearity evaluation method of Henry (1992) to be implemented with each CMB calculation. The maximum source uncertainty is a threshold expressed as a percentage of the total measured mass and is adjustable via the spinners (default = 20% ; acceptable range 0 - 100).

## Slide 12
Allows the eligible space collinearity evaluation method of Henry (1992) to be implemented with each CMB calculation. The minimum source projection is set to a default value of 0.95 (acceptable range 0.0 - 1.0), but can be changed in the display field.

## Slide 13
This parameter sets the number of decimal places displayed in the output window and output files. Depends on the units used in the input data files. Setting affects the display columns for source contributions estimates, measured species concentrations (ambient samples and source profiles), calculated contributions by species, as well as for inverse singular values. Adjusted by using the spinners. The default value is 5 and the maximum value is 6.

## Slide 14
The units used for reporting results may be changed via a pull-down menu. Other typical units are available, or one may be created (the number of characters is limited to 5 or less).

## Slide 15
File format for spreadsheet-type output is selected in the pull-down box. Default is ASCII (txt); comma-separated value (CSV) is also available. Selection is echoed on the status bar at the top of the screen.

## Slide 16
Checking this box applies the Britt and Luecke (1973) linear least squares solution explained by Watson et al. (1984) when applied to CMB calculations. Allows the source profiles used in the fit calculation to vary, and enables a general solution to the least squares estimation that includes uncertainty in all the variables (i.e., the source compositions as well as the ambient concentrations).

## Slide 18
Checking this box eliminates negative source contributions from the calculation, one at a time. After each fit attempt, if any sources have negative contributions, the source with the largest negative contribution is eliminated and another fit is attempted. Process is repeated until EPA-CMB8.2 finds no sources with negative contributions. Invocation of this option affects the fit obtained by effectively removing collinear sources.

## Slide 19
Causes the program to cycle through the corresponding pairs (same array index) of fitting species and source profile arrays specified in the source and species selection input windows until best composite Fit Measure has been achieved. The fit with the largest Fit Measure is then displayed and becomes the current fit. After a Best Fit has been made, the fitting species and fitting sources arrays will be tagged (highlighted) in their respective windows.

## Slide 20
Weights (coefficients) applied to each of the performance measures chi square, r-square, percent mass, and fraction of eligible sources. Positive values between 0 and 1 may be entered by typing into the appropriate display fields. Defaults are 1.0 for each performance measure weight.
Click

## Slide 21
Click

## Slide 22
Click
Collapsed list of samples.

## Slide 23
Click

## Slide 24
Click

## Slide 25
Click Index Number

## Slide 26
Click

## Slide 27
Click Index Number

## Slide 29
Click

## Slide 30
Click

## Slide 31
Click

## Slide 32
Click
Collapsed view for Array 5

## Slide 33
NB: Sample selection will be retained following the batch calculation. Samples can easily be DEselected and REselected on the Ambient Data Samples screen.
Click

## Slide 34
Click
Batch run for the 6 samples tagged …

## Slide 35
3rd result of the 6 in the buffer …
SUM

## Slide 36
Click
Print / Save Main Report
Click

## Slide 38
Click
Click

## Slide 40
Click
Click
Save spreadsheet-type results

## Slide 41
Click

## Slide 42
SPcode SPname I SiteID DATE ST DR SIZE Mconc Munc Cconc Cunc Rsquare CHIsqr %MASS SJV001 SOIL01
TMAC TMAU FELLOW 07/26/88 0 24 FINE 21.53630 1.19000 20.61957 1.05551 0.91276 4.86863 95.74332 4.72533 0.30812
N3IC N3IU * FELLOW 07/26/88 0 24 FINE 0.21280 0.18520 0.25688 0.05922 0.91276 4.86863 95.74332 0.01276 0.02221
S4IC S4IU * FELLOW 07/26/88 0 24 FINE 5.14750 0.27090 5.64551 0.50730 0.91276 4.86863 95.74332 0.00189 0.00614
N4TC N4TU * FELLOW 07/26/88 0 24 FINE 1.91540 0.13330 1.72104 0.17520 0.91276 4.86863 95.74332 0.00284 0.00236
KPAC KPAU * FELLOW 07/26/88 0 24 FINE 0.11510 0.02380 0.10179 0.03801 0.91276 4.86863 95.74332 0.00473 0.00142
NAAC NAAU * FELLOW 07/26/88 0 24 FINE 0.14880 0.05830 0.13499 0.03160 0.91276 4.86863 95.74332 0.00425 0.00189
ECTC ECTU * FELLOW 07/26/88 0 24 FINE 0.81720 0.19810 1.81263 0.49971 0.91276 4.86863 95.74332 0.12995 0.05434
OCTC OCTU * FELLOW 07/26/88 0 24 FINE 3.89260 0.45780 2.74572 0.61583 0.91276 4.86863 95.74332 0.48482 0.06521
ALXC ALXU * FELLOW 07/26/88 0 24 FINE 0.29510 0.03000 0.44982 0.05106 0.91276 4.86863 95.74332 0.44796 0.05103
SIXC SIXU * FELLOW 07/26/88 0 24 FINE 0.94330 0.06120 1.17369 0.13467 0.91276 4.86863 95.74332 1.15014 0.13042
SUXC SUXU _ FELLOW 07/26/88 0 24 FINE 2.01640 0.10200 1.83451 0.15798 0.91276 4.86863 95.74332 0.00945 0.00520
CLXC CLXU * FELLOW 07/26/88 0 24 FINE 0.02750 0.00710 0.05008 0.01515 0.91276 4.86863 95.74332 0.00331 0.00047
KPXC KPXU * FELLOW 07/26/88 0 24 FINE 0.16320 0.01060 0.14503 0.02987 0.91276 4.86863 95.74332 0.04867 0.00567
CAXC CAXU * FELLOW 07/26/88 0 24 FINE 0.17820 0.01160 0.09446 0.01020 0.91276 4.86863 95.74332 0.08836 0.00992
TIXC TIXU * FELLOW 07/26/88 0 24 FINE 0.02980 0.00690 0.02505 0.00288 0.91276 4.86863 95.74332 0.02457 0.00284
VAXC VAXU * FELLOW 07/26/88 0 24 FINE 0.03660 0.00370 0.03836 0.00275 0.91276 4.86863 95.74332 0.00142 0.00047
CRXC CRXU * FELLOW 07/26/88 0 24 FINE 0.00660 0.00180 0.00187 0.00090 0.91276 4.86863 95.74332 0.00142 0.00000
MNXC MNXU * FELLOW 07/26/88 0 24 FINE 0.00580 0.00100 0.00632 0.00075 0.91276 4.86863 95.74332 0.00520 0.00047
FEXC FEXU * FELLOW 07/26/88 0 24 FINE 0.27460 0.01830 0.28496 0.03120 0.91276 4.86863 95.74332 0.27549 0.03119
NIXC NIXU * FELLOW 07/26/88 0 24 FINE 0.03790 0.00230 0.03604 0.00405 0.91276 4.86863 95.74332 0.00047 0.00000
CUXC CUXU _ FELLOW 07/26/88 0 24 FINE 0.13830 0.06990 0.00059 0.00007 0.91276 4.86863 95.74332 0.00047 0.00000
ZNXC ZNXU _ FELLOW 07/26/88 0 24 FINE 0.09320 0.04160 0.01606 0.00178 0.91276 4.86863 95.74332 0.00095 0.00000
BRXC BRXU _ FELLOW 07/26/88 0 24 FINE 0.01080 0.00080 0.00708 0.00367 0.91276 4.86863 95.74332 0.00047 0.00000
PBXC PBXU * FELLOW 07/26/88 0 24 FINE 0.02310 0.00540 0.00900 0.00500 0.91276 4.86863 95.74332 0.00000 0.00000
Left-hand side of the spreadsheet-type output file …

## Slide 43
Click

## Slide 44
Click

## Slide 45
Modified Pseudo-Inverse Normalized Matrix